## Slide 1: Robotics 1
Industrial Robotics

## Slide 2: What is a robot?
industrial definition (RIA = Robotic Institute of America)
re-programmable multi-functional manipulator
designed to move materials, parts, tools, or specialized devices through variable programmed motions for the performance of a variety of tasks, which also acquire information from the environment
and move intelligently in response
ISO 8373:2012 definition
an automatically controlled, reprogrammable, multipurpose manipulator programmable in three or more axes, which may be either fixed in place or mobile for use in industrial automation applications
more general definition (“visionary”)
intelligent connection between perception and action

## Slide 3: Robots !!
Waseda WAM-8 (1984)
Comau H4 (1995)
Spirit Rover (2002)

## Slide 4: A bit of history
Robota (= “work” in slavic languages) are artificial human- like creatures built for being inexpensive workers in the theater play Rossum’s Universal Robots (R.U.R.) written by Karel Capek in 1920
Laws of Robotics by Isaac Asimov in I, Robot (1950)
  A robot may not injure a human being or, through inaction, allow a human being to come to harm
  A robot must obey orders given to it by human beings, except where such orders would conflict with the First Law
  A robot must protect its own existence as long as such protection does not conflict with the First or Second Law

## Slide 5: Evolution toward industrial robots
computer numerically controlled
machines (CNC)
mechanical telemanipulators
1950
robot manipulators
1970
Unimation PUMA
with respect to the ancestors
  flexibility of use
  adaptability to a priori unknown conditions
  accuracy in positioning
  repeatability of operation

## Slide 6: The first industrial robot
US Patent General Motor plant, 1961
G. Devol and J. Engelberger (Unimation)

## Slide 7: Historical pictures and clips
bimanual remote manipulation at Oak Ridge Nat’l Labs
Unimate 6-dof robots
video
video

## Slide 8: Robot manipulators
ASEA IRB-6 (1973)
first robot
all-electric-drives
Hirata AR-300 (1978)
first SCARA robot
Cincinnati Milacron T3 (1974)
first micro- computer controlled robot
Unimation PUMA 560
(1979)
6R with human-like dexterity

## Slide 9: robots – a 50-year journey robotics research up to 2000
Video compiled for the IEEE ICRA 2000 conference, S. Francisco

## Slide 10: World Robotics 2017
executive summary for 2017
statistics by IFR issued yearly in early October
(last one published; for 2018 edition + back issues since 2008, check course web site)
robotics market value in 2016: $13.1 billion (+18% over 2015); robot systems: $40 billion
total worldwide stock at end 2016: 1.8 million units of operational industrial robots (+12%)
highest ever robot sales worldwide in 2016 (~295K, +16%), for the fourth year in a row
China expanded further as the largest market since 2013, now with a 30% share (+3%)
75% of sales goes to 5 countries: first is China (87K, close to Europe + Americas = 97K), then Korea (41K, +10%/year average since 2011), Japan (38K, +10%), USA (31K, +14%), and Germany (20K, steady); Italy (6.7K, steady) is the 2nd market in Europe (7th worldwide)
main industrial drivers: automotive (35% of new robots, with moderate rate increase) and electrical/electronics (31%, catching up very fast; now first in Asia), followed by metal and machinery, rubber and plastics, food industry, ...
a continued accelerated growth!

## Slide 11: Diffusion industrial robots in operation worldwide
2008-2016
(as reference: industrial robots in stock in 1973 = 3K, in 1983 = 66K) length of robot service life is estimated in 12-15 years
2020*: ~3M robots in operation

## Slide 12: Diffusion industrial robots in operation by world area
2020*: ~1.9M robots in Asian factories ...
... out of which almost 1M operating in China!

## Slide 13: Diffusion robots in industrial sectors
Robotics 1
13
almost 70% of robots are in three main industries

## Slide 14: Annual supply new industrial robots worldwide
2017*-2020*: forecast of 1.7M new industrial robots
double-digit average annual increase
highest level ever: 294K new units

## Slide 15: Annual supply new robots by industrial sectors
continued increase in major industries

## Slide 16: Annual supply new industrial robots by world area
2020*: 40% of the global supply of new robots will go to China

## Slide 17: Annual supply new installations in top markets (countries)
in 2016: 5 markets account for 75% of total supply

## Slide 18: Annual supply market comparison of new industrial robots
China:
largest market since 2013
40% of global supply in 2019*
now also producing robots for their internal market...
Western EU:
Germany, Italy, France, Spain, and UK have a slow but steady increase

## Slide 19: Annual supply market comparison of new industrial robots
USA:
considerable increase since 2010
Germany:
moderate increase at record levels in Europe

## Slide 20: Density of robots
Robotics 1
20
number of robots per 10000 employees
in the manufacturing industry in 2015 (and 2016)
74
²303
631
488
Italy: degree of automation still relatively high, but not increasing in comparison to other countries
309
68
China
Average robot density in USA: 184, Europe: 99, Americas: 84, Asia: 63

## Slide 21: Density of robots
number of robots per 10000 employees
in the automotive and in all other industries in 2015 (and 2016)
Italy was at 2nd place in 2011!
comparatively still low density
in general industry
1261
2145!!
1150
  1051
²1240
²1131

## Slide 22: A long-range trend in robot prices
An articulated industrial robot with six degrees of freedom of medium size costs about 80-100 KEuro

## Slide 23: Industrial robot and its auxiliary equipments
Comau SMART H robot
C3G Plus controller
Welding control box
Application software
Air/water supply
SWIM Board
Integrated cables
Welding gun
Auxiliary devices in the robotic cell
(servo-controlled axes)
SWIM = Spot Welding Integrated Module

## Slide 24: ABB IRB 7600
commercial video by ABB

## Slide 25: Industrial applications
manipulation (pick-and-place)
assembly
spray painting and coating
arc welding
spot welding with pneumatic or servo-controlled gun
laser cutting and welding
gluing and sealing
mechanical finishing operations (deburring, grinding)

## Slide 26: A day in the life of an industrial robot
At BMW car production line with ABB robots
video video
pick-and-place
with end-effector to reorient part
pick-and-place
with support to reorient part

## Slide 27: A day in the life of an industrial robot
video video
pick-and-place
heavy parts and human intervention
metal cutting
on a supporting machine with dofs (video speeded up at some point)

## Slide 28: A day in the life of an industrial robot
video video
glue deposit
(on fancy paths!)
cooperation of multiple robots
for handling and sealing a car body

## Slide 29: A day in the life of an industrial robot
video video
coating parts
for rust and corrosion protection
spray painting

## Slide 30: A day in the life of an industrial robot
video video
hood deburring
with a suspended tool
test measurements
with assembly on a AGV

## Slide 31: What a robot should do and what cannot do
video
spray painting
very unhealthy for human operators
assembly of flexible or complex parts
(here a car dashboard)
video
yet
⇒ human-robot collaboration (co-bots or co-workers)

## Slide 32: Plasma cutting
video
small KUKA robot used for plasma cutting of a stainless steel toilet (courtesy of Engenious Solutions Pty)
nozzle
hot plasma
electrode
gas chamber

## Slide 33: Robotized workcells

## Slide 34: 3D simulation of robotic tasks
analysis of operative cycle times
off-line programming and optimization
layout design and collision checking
3D graphic simulation

## Slide 35: Welding - 1
spot with servo-controlled gun
stud welding

## Slide 36: Welding - 2
spot (discrete) or arc (continuous)

## Slide 37: Two cooperating robots in welding
ABB video at Laxa, Sweden

## Slide 38: Palletizing
pallet = a portable platform on which goods can be moved, stacked, and stored

## Slide 39: Palletizing of cheese forms
using Kawasaki robots (courtesy of Effedue Engineering)
video

## Slide 40: Folding
with loading of sheets under the press

## Slide 41: Deburring
car windshields may have large manufacturing tolerances and a sharp contour profile
the robot follows a given predefined Cartesian path
the contact force between cutting blade and glass must be feedback controlled
deburring robot head mounts a force load cell and is pneumatically actuated

## Slide 42: Deburring center
deburring center for steel parts
using Comau SMART NJ 110-3.0/foundry robot (courtesy of Adami srl)
video

## Slide 43: Off-line robot workstation
articulated robot in metal surface finishing operation

## Slide 44: Safety in robotic cells
commercial video from ABB
SafeMove (2008) cell monitoring system: no fences!

## Slide 45: Robot manipulator kinematics
Comau Smart H4
closed kinematic chain
Kuka 150_2 (series 2000)
open kinematic chain (rigid bodies connected by joints)
Fanuc F-200iB
parallel kinematics

## Slide 46: SCARA-type robots
SCARA (Selective Compliant Arm for Robotic Assembly)
4 degrees of freedom (= joints): 3 revolute + 1 prismatic (vertical) axes
compliant in horizontal plane for micro-assembly and pick-and-place
Mitsubishi RP
(repeatability 5 micron,
payload 5 kg)
Mitsubishi RH
(workspace 850 mm,
velocity 5 m/s)
Bosch Turbo

## Slide 47: Adept Cobra i600
fastest SCARA robot for pick-and-place tasks!
video

## Slide 48: Other types of robots
Comau Mast gantry robot
(payload up to 560 kg)
ABB Flexpicker
(150 pick-and-place operations/minute)

## Slide 49: Chocolate packaging with lightweight parallel robots
test video with ABB Flexpicker
video with Adept Quatro s650

## Slide 50: Distribution by robot type
for 59600 articulated robots installed back in 2004
(90% of all robots installed in America, 74% in Europe, only 49% in Asia)
of kinematic configuration

## Slide 51: Robot data sheet
Fanuc
R-2000i/165F

## Slide 52: Workspace

## Slide 53: Visualization of workspace and mobility
kinematic simulation of a 6-dof Comau robot (all revolute joints)
video

## Slide 54: Visualization of workspace and mobility
V-REP simulation of the 7-dof KUKA LWR4+ robot (all revolute joints)
video

## Slide 55: Robot end-effector sensors and tools

## Slide 56: Calibration of robot kinematics

## Slide 57: Man-machine interface
teach-box pendant used as robot programming interface
cabinet with power electronics for robot supervision and control

## Slide 58: Programming and control environment
control modules and interfaces (Reis Robotics)

## Slide 59: Motion programming and scaling
commercial video from ABB
TrueMove & QuickMove fast motion control performance

## Slide 60: Mobile base robots in industry
AGV (Automated Guidance Vehicles) for material and parts transfer on the factory floor: wire- or laser-driven along predefined paths

## Slide 61: Lifting AGV for warehouses
video by Elettric80

## Slide 62: Kiva Systems
company acquired in 2012 for $775 million by Amazon (store automation)

## Slide 63: Intelligent AGV in factories
commercial video of ADAM mobile robot (RMT Robotics)

## Slide 64: What’s next in industrial robotics?
changing nature of manufacturing and work
shift from high volume/low mix to low volume/high mix is having a profound impact on manufacturing
many industries are facing acute shortages of skilled labor
quicker return-of-investment (ROI) of automation and rising wages are eventually discouraging labour arbitrage
increased focus is being placed on workplace safety
Source: Steven Wyatt (IFR). “Today’s trends, tomorrow’s robots!” Frankfurt, 27 September 2017

## Slide 65: What’s next in industrial robotics?
addressing some real facts opens huge opportunities
answers to these challenges lie in Simplification, Digitalisation, and Collaboration

## Slide 66: What’s next in industrial robotics?
Simplification (critical for SME, but also for large global manufacturers)
robots easier to install, program (with open source) and operate will unlock entry barriers to the large market of small and medium enterprises (SMEs)
trend towards having production closer to the end consumer is driving the importance of standardisation & consistency across global brands
Digitalisation (Big Data allows taking better decisions on factory operations)
“Industry 4.0”, linking the real-life factory with a virtual/digital one, will play an increasingly important role in global manufacturing
vision and sensing devices, coupled with analytics platforms, will pave the way for new industry business models
IoT/AI/Machine Learning will drive many robotics developments in coming years
Collaboration
collaborative robots are shifting the traditional limits of “what can be automated?”
collaborative robots increase manufacturing flexibility as ‘low-volume, high-mix’ becomes the main standard
collaboration is also about productivity with increased physical and cognitive
human/robot interaction

## Slide 67: What’s next in industrial robotics?
connected and collaborative robots will enable SMART Manufacturing for both SMEs & Global Enterprises
robots doing the same task connect across all global locations so performance can be easily compared and improved
“connected” future of robotics
self-optimizing production
robots automatically download what they need to get started from a cloud library and then optimize through “self-learning”
self-programming robots

## Slide 68: Franka Emika robot
... one possible example (dated 2016)
video