## Slide 1: Robotics 1
Robot components:
Actuators
1

## Slide 2: Robot as a system
Robot
program of tasks
working environment
commands
actions
mechanical units
sensor units
actuation units
supervision units
2

## Slide 3: Functional units of a robot
3
mechanical units (robot arms)
  rigid links connected through rotational or prismatic joints (each 1 dof)
  mechanical subdivisions:
    supporting structure (mobility), wrist (dexterity), end-effector (task execution, e.g., manipulation)
sensor units
  proprioceptive (internal robot state: position and velocity of the joints)
  exteroceptive (external world: force and proximity, vision, …)
actuation units
  motors (electrical, hydraulic, pneumatic)
  motion control algorithms
supervision units
  task planning and control
  artificial intelligence and reasoning

## Slide 4: Actuation systems
power supply
power amplifier
servomotor
transmission
(mechanical gears)
Pc
Pp
Pda
Pds
Pdt
Pa
Pm
Pu
mechanical
electrical, hydraulic, or pneumatic
P = types of powers in play
Robotics 1
4
electrical
power losses due to dissipative effects (e.g., friction)
power = force · speed = torque · angular speed [Nm/s, W] efficiency = power out / power in [%]

## Slide 5: Motion transmission gears
optimize the transfer of mechanical torque from actuating motors to driven links
quantitative transformation (from low torque/high velocity to high torque/low velocity)
qualitative transformation (e.g., from rotational motion of an electrical motor to a linear motion of a link along the axis of a prismatic joint)
allow improvement of static and dynamic performance by reducing the weight of the actual robot structure in motion (locating the motors remotely, closer to the robot base)

## Slide 6: Transmissions in robotics
spur gears: modify direction and/or translate axis of (rotational or translational) motor displacement
  problems: deformations, backlash
lead screws, worm gearing: convert rotational into translational motion (prismatic joints)
  problems: friction, elasticity, backlash
toothed belts and chains: dislocate the motor
w.r.t. the joint axis
    problems: compliance (belts) or vibrations induced by larger mass at high speed (chains)
harmonic drives: compact, in-line, power efficient, with high reduction ratio (up to 150-200:1)
  problems: elasticity
transmission shafts: long, inside the links, with flexible couplings for alignment

## Slide 7: Transmission gears in motion
racks and pinion
  one rack moving (or both)
epi-cycloidal gear train
  or hypo-cycloidal (small gear inside)
planetary gear set
  one of three components is locked: sun gear, planet carrier, ring gear
video
video
video

## Slide 8: Harmonic drives
input from motor
output to load
Wave Generator (C) of slightly elliptic external form
(with ball bearings)
Circular Spline (A)
inner #teeth CS = outer #teeth FS + 2 reduction ratio
n = #teeth FS / (#teeth CS - #teeth FS)
= #teeth FS / 2
FlexSpline (B) (two contact points)

## Slide 9: Operation of an harmonic drive
commercial video by Harmonic Drives AG

## Slide 10: Optimal choice of reduction ratio
transmission gear
Pdt
Pm Pu
motor
link
power dissipated by friction
ideal case (no friction)
. .
m = n u Tu = n Tm
for minimizing Tm, we set: Tm = (Jm - Ju /n2) a = 0
n = (Ju / Jm)1/2
n
“matching” condition between inertias
. .
Pm = Tm m = Tu u = Pu
torque × angular speed
n = reduction ratio (≫1)
.. ..
to have u = a (thus m = n a), the motor should provide a torque
.. ..
Tm = Jm m + 1/n (Ju u) = (Jm n + Ju /n) a
inertia × angular acceleration

## Slide 11: Transmissions in industrial robots
Robotics 1
11
PUMA 260: 1st axis
transmissions used (inside) 6-dof Unimation industrial robots with serial kinematics
PUMA 560
PUMA 560: 2nd and 3rd axes
PUMA 560: inner and outer links
PUMA 560: last 3 axes

## Slide 12: Inside views on joint axes 4, 5 & 6 of an industrial KUKA robot
looking inside the forearm to see the transmissions of the spherical wrist
motor rotation seen from the encoder side (small couplings exist)
Robotics 1
12
video
video

## Slide 13: Desired characteristics for robot servomotors
low inertia
high power-to-weight ratio
high acceleration capabilities
  variable motion regime, with several stops and inversions
large range of operational velocities
  1 to 2000 rpm (round per min)
high accuracy in positioning
  at least 1/1000 of a turn
low torque ripple
  continuous rotation at low speed
power: 10W to 10 kW

## Slide 14: Servomotors
pneumatic: pneumatic energy (compressor) 
pistons or chambers  mechanical energy
  difficult to control accurately (change of fluid compressibility)  no trajectory control
  used for opening/closing grippers
  ... or as artificial muscles (McKibben actuators)
hydraulic: hydraulic energy (accumulation tank)
 pumps/valves  mechanical energy
  advantages: no static overheating, self-lubricated, inherently safe (no sparks), excellent power-to-weight ratio, large torques at low velocity (w/o reduction)
  disadvantages: needs hydraulic supply, large size, linear motion only, low power conversion efficiency, high cost, increased maintenance (oil leaking)

## Slide 15: Electrical servomotors
advantages
  power supply available everywhere
  low cost
  large variety of products
  high power conversion efficiency
  easy maintenance
  no pollution in working environment
disadvantages
  overheating in static conditions (in the presence of gravity)
    use of emergency brakes
  need special protection in flammable environments
  some advanced models require more complex control laws

## Slide 16: Electrical servomotors for robots
Va
direct current (DC) motor
collector
brushes
stator (permanent magnets)
stator
switching circuit
V1 V2 Vn
V
a
with electronic switches (brushless)
rotor (main motor inertia)

armature circuit

## Slide 17: Advantages of brushless motors
reduced losses, both electrical (due to tension drops at the collector-brushes contacts) and mechanical (friction)
reduced maintenance (no substitution of brushes)
easier heat dissipation
more compact rotor (less inertia and smaller dimensions)
… but indeed a higher cost!

## Slide 18: Principle of operation of a DC motor
video
T
T
T
DC supply
Va
permanent magnets N-S
commutator ring (to switch direction
of armature current every half round)
single coil (armature)
1 pole pair ...
... + commutator multiple pole pairs
less torque ripple!
"⃗ = $ %⃗ × ' ( = ) "⃗

## Slide 19: Characteristic curves of a DC motor
conversion SI ⇔ US unit systems (!!)
1 Nm = 141.61 oz-in
100 oz-in = 0.70 Nm
medium size motor 160W
small size motor 5.5W
stall load torque
stall current
no-load max speed
rated operating point
at steady-state, for constant applied tension Va

## Slide 20: DC electrical motor mathematical model for command and control
kv = kt
electrical balance
mechanical balance
Tm = (sIm + Fm)  + Tload
Tm = kt Ia
(energy balance, in SI units!)
−
- -
-
-
+
T
load
Tm


Va
+
I
a
Vemf
Vc
V’
c
+
Ci(s)
G
v
1+sTv
1
sLa
Ra
k
t
k
v
Fm
1
sIm
1
s
ki
ki = 0  velocity generator* ki Ci(0) Gv ≫ Ra  torque generator*
Va = (Ra + sLa) Ia + Vemf
Vemf = kv  (back emf)
current loop
Laplace domain (transfer functions)
DC motor
* = the motor is seen here as a steady state “generator”; to actually regulate velocity or torque in an efficient way against Tload, further control loops are needed!

## Slide 21: Data sheet electrical motors
DC drives
nominal/peak torques and speeds
Max. Instant. Torque

## Slide 22: Data sheet electrical motors
AC drives
for applications requiring a rapid and accurate response (in robotics!)
induction motors driven by alternate current (AC)
small diameter rotors, with low inertia for fast starts, stops, and reversals

## Slide 23: Exploded view of a joint in the DLR-III robot
!
"
stiffness #
joint torque
$% = #(! − ")