## Slide 1
Block Diagram

## Slide 2: Need of Block Diagram Algebra
If the system is simple & has limited parameters then it
is easy to analyze such systems using the methods discussed earlier i.e. transfer function, if the system is complicated and also have number of parameters then it is very difficult to analyze it.

## Slide 3
block
diagram
It is a simple way to represent any practically complicated system. In this each component of the system is represented by a separate block known as functional block.
These blocks are interconnected in a proper sequence.
Need of Block Diagram Algebra
To overcome this problem representation method is used.

## Slide 4: Block Diagram Fundamentals
Block Diagram: It is shorthand, pictorial representation
of the cause and effect relationship between input and output of a physical system.
BLOCK
Input
Output

## Slide 5: Block Diagram Fundamentals
Output: The value of the input is multiplied to the value of block gain to get the output.
3s
X(s)
Y(s)
Output
Y(s)= 3s. X(s)

## Slide 6: Block Diagram Fundamentals
Output =x+y-z
+
x
-
z
Summing Point: Two or more signals can be added/ substracted at summing point.
y
+
output

## Slide 7: Block Diagram Fundamentals
Take off Point: The output signal can be applied to two or more points from a take off point.
Z
Z
Z
Z
Take off point
103

## Slide 8: Block Diagram Fundamentals
G1
G2
H1
-
R(s) +
C(s)
Forward Path: The direction of flow of signal is from input to output
Forward Path
Feedback Path
Feedback Path: The direction of flow of signal is from output to input

## Slide 9: Block Diagram Reduction Techniques
Rule 1: For blocks in cascade
Gain of blocks connected in cascade gets multiplied with each other.
G1
R(s)
R1(s) G2
C(s)
R1(s)=G1R(s)
C(s) =G2R1(s)
=G1G2R(s)
C(s)= G1G2R(s)
G1G2
R(s)
C(s)

## Slide 10
G1
G2
G3
R(s)
C(s)
Find Equivalent
G1G2G3
R(s)
C(s)

## Slide 11
G1
G2
G3
R(s)
C(s)
R1(s)
Find Equivalent
G1G2G3
R(s)
C(s)
G1G2
R(s)
C(s)
G3
R1(s)
107

## Slide 12: Block Diagram Reduction Techniques
Rule 2: For blocks in Parallel
Gain of blocks connected in parallel gets added algebraically.
C(s)= (G1-G2+G3) R(s)
G1-G2+G3
R(s)
C(s)
G1
G2
R(s)
C(s)
G3
R1(s)
R3(s)
+
+
R2(s) -
C(s)= R1(s)-R2(s)+R3(s)
= G1R(s)-G2R(s)+G3R(s)
C(s)=(G1-G2+G3) R(s)

## Slide 13: Block Diagram Reduction Techniques
Rule 3: Eliminate Feedback Loop
C(s)
G
H
R(s)
+
+-
R(s)
C(s)
G
1  GH
B(s)
E(s)
C(s)
G
R(s)

1  GH
In General

## Slide 14
R(s)
C(s)
G
H
B(s)
E(s)
+-
From Shown Figure,
and
E(s)  R(s)  B(s)
C(s)  G.E(s)
 G[R(s)  B(s)]
 GR(s)  GB(s)
B(s)  H.C(s)
C(s)  G.R(s)  G.H.C(s)
C(s)  G.H  GR(s)
C(s){1 G.H}  G.R(s)
 C(s)  G R(s) 1  GH
But
For Negative Feedback

## Slide 15
R(s)
C(s)
G
H
B(s)
E(s)
++
and
But
For Positive Feedback
From Shown Figure,
E(s)  R(s)  B(s)
C(s)  G.E(s)
 G[R(s)  B(s)]
 GR(s)  GB(s)
B(s)  H.C(s)
C(s)  G.R(s)  G.H.C(s)
C(s)  G.H  GR(s)
C(s){1 G.H}  G.R(s)
 C(s) G R(s) 1  GH
111

## Slide 16: Block Diagram Reduction Techniques
Rule 4: Associative Law for Summing Points
The order of summing points can be changed if two or more summing points are in series
C(s)
B2
R(s) +
X +
-
C(s)
B1
R(s) +
X +
-
B1
X=R(s)-B1
C(s)=X-B2
C(s)=R(s)-B1-B2
B2
X=R(s)-B2
C(s)=X-B1 C(s)=R(s)-B2-B1

## Slide 17: Block Diagram Reduction Techniques
Rule 5: Shift summing point before block
R(s)
C(s)
X
+
G
C(s)=R(s)G+X
C(s)=G{R(s)+X/G}
=GR(s)+X
+
C(s)
R(s) +
G
1/G
X
+

## Slide 18: Block Diagram Reduction Techniques
Rule 6: Shift summing point after block
C(s)
R(s) +
G
X
C(s)=G{R(s)+X}
=GR(s)+GX
C(s)=GR(s)+XG
=GR(s)+XG
+
R(s)
C(s)
X
+
G
G
+

## Slide 19
Block Diagram Reduction Techniques
Rule 7: Shift a take off point before block
R(s)
C(s)
G
C(s)=GR(s)
and X=C(s)=GR(s)
C(s)=GR(s)
and X=GR(s)
X
R(s)
C(s)
X
G
G

## Slide 20: Block Diagram Reduction Techniques
Rule 8: Shift a take off point after block
R(s)
C(s)
X
C(s)=GR(s)
and X=C(s).{1/G}
=GR(s).{1/G}
= R(s)
G
R(s)
C(s)
G
X
1/G
C(s)=GR(s)
and X=R(s)
116

## Slide 21: Block Diagram Reduction Techniques
While solving block diagram for getting single block
equivalent, the said rules need to be applied. After each simplification a decision needs to be taken. For each decision we suggest preferences as

## Slide 22: Block Diagram Reduction Techniques
First Choice
First Preference:
Rule 1 (For series)
Second Preference:
Rule 2 (For parallel)
Third Preference:
Rule 3 (For FB loop)

## Slide 23
Block Diagram Reduction Techniques
Second Choice
(Equal Preference)
Rule 4 Adjusting summing order
Rule 5/6 Shifting summing point before/after block Rule7/8 Shifting take off point before/after block

## Slide 24: Example 1
-
+
-
+
+
G1
H1
G2
G3
G4
G5
H2
G6
+
R(s) +
C(s)

## Slide 25
Rule 1 cannot be used as there are no immediate series blocks.
Hence Rule 2 can be applied to G4, G3, G5 in parallel to get an equivalent of G3+G4+G5

## Slide 26: Example 1
-
+
-
+
+
G1
H1
G2
G3
G4
G5
H2
G6
+
R(s) +
C(s)
Apply Rule 2
Blocks in Parallel
cont….

## Slide 27: Example 1
-
+
-
G1
H1
G2
H2
G6
R(s) +
C(s)
G3+G4+G5
Apply Rule 1
Blocks in series
cont….

## Slide 28: Example 1
+
-
+
-
G1
H1
H2
G6
R(s)
C(s)
G2(G3+G4+G5)
Apply Rule 3
Elimination of feedback loop
cont….

## Slide 29: Example 1
-
H2
G6
R(s) +
C(s)
G2(G3+G4+G5)
Apply Rule 1
Blocks in series
G1
1  G1H1
cont….

## Slide 30: Example 1
-
H2
G6
R(s) +
C(s)
Apply Rule 3
Elimination of feedback loop
G1G2(G 3  G 4  G 5) 1  G1H1
cont….

## Slide 31: Example 1
G6
R(s)
C(s)
Apply Rule 1
Blocks in series
G1G2(G 3  G 4  G 5)
1  G1H1  G1G2H 2(G 3  G 4  G 5)
cont….

## Slide 32: Example 1
R(s)
C(s)
G1G2G6(G 3  G 4  G 5)
1  G1H1  G1G2H 2(G 3  G 4  G 5)
cont….

## Slide 33: Example 1
G1G2G6(G 3  G 4  G 5)
1  G1H1  G1G2H 2(G 3  G 4  G 5)
R(s)
C (s) 
cont….

## Slide 34: Example 2
G1
H1
G2
G3
G4
H2
C(s)
R(s) +
+
+
+
+
-

## Slide 35: Example 2
G1
H1
G2
G3
G4
H2
C(s)
R(s) +
+
+
+
+
-
Apply Rule 1 Blocks in series
cont….

## Slide 36: Example 2
G1G2
H1
G3
G4
H2
C(s)
R(s) +
+
+
+
+
-
Apply Rule 2 Blocks in parallel
cont….

## Slide 37: Example 2
G1G2
H1
G3+G4
H2
C(s)
R(s) +
+
+
-
Apply Rule 3
Elimination of feedback loop
cont….

## Slide 38: Example 2
G3+G4
H2
C(s)
R(s) +
+
Apply Rule 2
Blocks in series
G1G2
1  G1G2H1
cont….

## Slide 39: Example 2
H2
C(s)
R(s) +
+
Apply Rule 3
Elimination of feedback loop
G1G2(G 3  G 4) 1  G1G2H1
cont….

## Slide 40: Example 2
R(s)
C(s)
G1G2(G 3  G 4)
1  G1G2H1  G1G2G3H 2  G1G2G4H 2
cont….

## Slide 41: Example 2
R(s)
G1G2(G 3  G 4)
C(s) 
1  G1G2H1  G1G2G3H 2  G1G2G4H 2
cont….

## Slide 42: Example 3
H1
G2
G3
H2
C(s)
R(s) +
+
+
+
-
-
G1
G4
G5

## Slide 43: Example 3
H1
G2
G3
H2
C(s)
R(s) +
+
+
-
G1
G4
G5
Apply Rule 3
Elimination of feedback loop
cont….
+
-

## Slide 44: Example 3
G3
H2
C(s)
R(s) +
+
+
-
G1
G4
G5
Apply Rule 1
Blocks in series
G2
1  G2H1
cont….

## Slide 45: Example 3
H2
C(s)
R(s) +
+
+
-
G4
G5
Apply Rule 2
Blocks in parallel
G1G2G3 1  G2H1
cont….

## Slide 46: Example 3
H2
C(s)
R(s) +
-
G4
Apply Rule 1 Blocks in series
G5  G1G2G3
1  G2H1
cont….

## Slide 47: Example 3
H2
C(s)
R(s) +
-
Apply Rule 3
Elimination of feedback loop
G 4(G5  G1G2G3 )
1  G2H1
cont….

## Slide 48: Example 3
R(s)
C(s)
G4G5  G2G4G5H1  G1G2G3G4
1 G2H1 G4G5H 2  G2G4G5H1H 2  G1G2G3G4H 2
cont….

## Slide 49: Example 3
R(s)
G4G5  G2G4G5H1  G1G2G3G4
C(s) 
1  G2H1  G4G5H 2  G2G4G5H1H 2  G1G2G3G4H 2
cont….

## Slide 50: Example 4
G1
H2
G2
H1
C(s)
R(s) +
+
-
-
-
+

## Slide 51: Example 4
G1
H2
G2
H1
C(s)
R(s) +
+
-
-
+
Apply Rule 3
Elimination of feedback loop
cont….
-

## Slide 52: Example 4
G1
H1
C(s)
R(s) +
+
-
-
G2
1  G2H 2
cont….

## Slide 53
Now Rule 1, 2 or 3 cannot be used directly.
There are possible ways of going ahead.
  Use Rule 4 & interchange order of summing so that Rule 3 can be used on G.H1 loop.
b. Shift take off point after
block reduce
by Rule 1, followed by Rule 3.
Which option we have to use????
G2
1  G2H 2

## Slide 54: Example 4
G1
H1
C(s)
+
-
-
Apply Rule 4
Exchange summing order
G2
1  G2H 2
1
R(s) +
2
cont….

## Slide 55: Example 4
G1
H1
C(s)
+
-
-
Apply Rule 3 Elimination feedback loop
G2
1  G2H 2
1
2
R(s) +
cont….

## Slide 56: Example 4
C(s)
-
Apply Rule 1 Bocks in series
G2
1  G2H 2
2
R(s) +
G1
1  G1H1
cont….

## Slide 57: Example 4
C(s)
-
OR
Now which Rule will be applied
-------It is blocks in parallel
-------It is feed back loop
2
R(s) +
G1G2
1  G1H1  G2H 2  G1G2H1H 2
cont….

## Slide 58: Example 4
C(s)
-
2
R(s) +
G1G2
1  G1H1  G2H 2  G1G2H1H 2
Let us rearrange the block diagram to understand Apply Rule 3 Elimination of feed back loop
cont….

## Slide 59: Example 4
R(s)
C(s)
G1G2
1  G1H1  G2H 2  G1G2H1H 2  G1G2
cont….

## Slide 60: Example 4
G1G2
R(s)
C(s) 
1  G1H1  G2H 2  G1G2H1H 2  G1G2
cont….

## Slide 61: Note 1: According to Rule 4
By corollary, one can split a summing point to two summing point and sum in any order
G
H
+
-
R(s) +
C(s)
B
G
H
+
-
R(s)
C(s)
B
+ +

## Slide 62: Example 5
G1
H1
C(s)
R(s) +
+
-
G2
G3
H2
H3
-
Simplify, by splitting second summing point as
said in note 1
-

## Slide 63: Example 5
G1
H1
C(s)
+
+
-
-
G2
G3
H2
H3
+
-
R(s)
Apply rule 3
Elimination of feedback loop
cont….

## Slide 64: Example 5
C(s)
+
-
G2
G3
H2
H3
+
-
R(s)
Apply rule 1
Blocks in series
G1
1  G1H1
cont….

## Slide 65: Example 5
C(s)
+
-
G3
H2
H3
+
-
R(s)
Apply rule 3
Elimination of feedback loop
G1G2
1  G1H1
cont….

## Slide 66: Example 5
C(s)
G3
H3
+
-
R(s)
Apply rule 1
Blocks in series
G1G2
1  G1H1  G1G2H 2
cont….

## Slide 67: Example 5
C(s)
H3
+
-
R(s)
Apply rule 3
Elimination of feedback loop
G1G2G3
1  G1H1  G1G2H 2
cont….

## Slide 68: Example 5
C(s)
R(s)
G1G2G3
1  G1H1  G1G2H 2  G1G2G3H 3
cont….

## Slide 69: Example 5
G1G2G3
R(s)
C(s) 
1  G1H1  G1G2H 2  G1G2G3H 3
cont….

## Slide 70: Example 6
H1
G2
G3
H2
C(s)
R(s) +
+
-
-
G1
G4
G5
+
+
Apply rule 8
Shift take off point beyond block G3

## Slide 71: Example 6
H1
G2
G3
H2
C(s)
R(s) +
+
-
-
G1
G4
G5
+
+
Apply rule 1 Blocks in series
1/ G3
cont….

## Slide 72: Example 6
H1
G2G3
H2
C(s)
R(s) +
+
-
-
G1
G4
+
+
Apply rule 2 Blocks in parallel
G5/ G3
cont….

## Slide 73: Example 6
H1
G2G3
H2
C(s)
R(s) +
+
-
-
G1
G4+(G5/
G3)
Apply rule 3 Feedback loop
cont….

## Slide 74: Example 6
H2
C(s)
R(s) +
-
G1
G4+(G5/
G3)
Apply rule 1 Blocks in series
G2G3
1 G2G3H1
cont….

## Slide 75: Example 6
H2
C(s)
R(s) +
-
(G1)(
G2G3
G3
)(G 4  G5)
1 G2G3H1
cont….

## Slide 76
G2G3
G3
 (G1)(
)(G 4  G5)
1 G2G3H1
 G1G2(G 4 G 3  G 5) 1  G2G3H1
G2G3
)(G 4G3  G5)
 (G1)(
1 G2G3H1 G3
Example 6
cont….

## Slide 77: Example 6
H2
C(s)
R(s) +
-
G1G2(G 4 G 3  G 5) 1  G2G3H1
Apply rule 3
Feedback loop
cont….

## Slide 78: Example 6
 | G1G2(G 4 G 3  G 5)
1  G2G3H1  G1G2H 2(G 3G 4  G 5) | 
R(s)
C(s)
cont….

## Slide 79: Example 6
R(S)
G1G2(G 4 G 3  G 5)
C(S) 
1  G2G3H1  G1G2H 2(G 3G 4  G 5)
cont….

## Slide 80: Example 7
H3
G2
H1
C(s)
R(s) +
+
-
-
G1
G3
H2
-
+
Apply rule 8
Shift take off point after block G4
G4

## Slide 81: Example 7
H3
G2
H1
C(s)
R(s) +
+
-
-
G1
G3
H2
-
+
Apply rule 1
Blocks in series
G4
1/G4
cont….

## Slide 82: Example 7
H3
G2
H1
C(s)
R(s) +
+
-
-
G1
G3G4
-
+
Apply rule 3
Feedback loop
H2/
G4
cont….

## Slide 83: Example 7
G2
H1
C(s)
R(s) +
+
-
-
G1
Apply rule 1
Blocks in series
H2/
G4
G3G4
1  G3G4H 3
cont….

## Slide 84: Example 7
H1
C(s)
R(s) +
+
-
-
G1
Apply rule 3
Feedback loop
H2/ G4
G2G3G4 1  G3G4H 3
cont….

## Slide 85: Example 7
H1
C(s)
R(s) +
-
G1
Apply rule 1
Blocks in series
G2G3G4
1  G3G4H 3  G2G3H 2
cont….

## Slide 86: Example 7
H1
C(s)
R(s) +
-
Apply rule 3
Feedback loop
G1G2G3G4
1  G3G4H 3  G2G3H 2
cont….

## Slide 87: Example 7
R(s)
C(s)
G1G2G3G4
1  G3G4H 3  G2G3H 2  G1G2G3G4H1
cont….

## Slide 88: Example 7
G1G2G3G4
R(S)
C(S) 
1  G3G4H 3  G2G3H 2  G1G2G3G4H1
cont….

## Slide 89: Example 8
G1
H2
G2
G3
C(s)
- -
G4
+
+
H1
-
Simplify, by splitting 3rd summing point as given in Note 1
1
R(s) +
2
+
3

## Slide 90: Example 8
G1
H2
G2
G3
C(s)
R(s) +
+
- -
G4
+
H1
-
Apply Rule 3
Elimination of Feedback loop
+ +
cont….

## Slide 91: Example 8
G1
H2
G2
G3
C(s)
R(s) +
+
- -
+
+
Apply Rule 8
Shift take off point after block
G4 1  G4H1
cont….

## Slide 92: Example 8
G1
H2
G2
G3/
G2
C(s)
R(s) +
+
- -
+
+
Apply Rule 1 Blocks in series
G4 1  G4H1
cont….

## Slide 93: Example 8
G1G2
H2
C(s)
R(s) +
+
- -
+
+
Now which rule we have to use?
G3/
G2
G4 1  G4H1
cont….

## Slide 94: Example 8
G1G2
H2
G3/
G2
C(s)
R(s) +
+
- -
+
+
Apply Rule 2 Blocks in parallel
G4 1  G4H1
1
cont….

## Slide 95: Example 8
G1G2
H2
C(s)
R(s) +
+
- -
Apply Rule 1
Blocks in series
G4 1  G4H1
G3  1
G2
cont….

## Slide 96: Example 8
G1G2
H2
C(s)
R(s) +
+
- -
Apply Rule 3
Elimination of Feedback Loop
(G 3  G 2)G4 G 2(1  G4H1)
cont….

## Slide 97: Example 8
C(s)
R(s) +
-
Apply Rule 1
Blocks in series
(G 3  G 2)G4 G 2(1  G4H1)
G1G2
1  G1G2H 2
cont….

## Slide 98: Example 8
C(s)
R(s) +
-
Apply Rule 3
Elimination of Feedback loop
G1G4(G 3  G 2)
(1  G1G 2 H 2)(1  G4H1)
cont….

## Slide 99: Example 8
R(s)
C(s)
G1G4(G 3  G 2)
1 G 4 H1 G1G2H 2  G1G2G4H1H 2  G1G4(G 2  G 3)
cont….

## Slide 100: Example 8
R(s)
G1G4(G 3  G 2)
C(s) 
1  G 4 H1  G1G2H 2  G1G2G4H1H 2  G1G4(G 2  G 3)
cont….

## Slide 101: Example 9
H2
G2
H3
C(s)
R(s) +
-
G1
G3
-
+
Apply rule 2
Blocks in Parallel
G5
H1
+
+ -
G4
+

## Slide 102: Example 9
H2
G2
H3
C(s)
R(s) +
+
-
-
G1+G4+ G5
G3
-
+
Apply rule 3
Elimination of Feedback Loop
H1
cont….

## Slide 103: Example 9
H3
C(s)
R(s) +
-
G1+G4+G5
Apply rule 1
Blocks in Series
G2
1  G2H1
G3
1  G3H 2
cont….

## Slide 104: Example 9
H3
C(s)
R(s) +
-
Apply rule 3
Elimination of Feedback loop
G2G3(G1  G 4  G 5) (1  G2H1)(1  G 3 H 2)
cont….

## Slide 105: Example 9
R(s)
C(s)
G2G3(G1  G 4  G 5)
1  G2H1  G3H 2  G2G3H1H 2  G2G3H 3(G1  G 4  G 5)
cont….

## Slide 106: Example 9
C(s)  G2G3(G1  G 4  G 5)
R(s) 1  G2H1  G3H 2  G2G3H1H 2  G2G3H 3(G1  G 4  G 5)
cont….

## Slide 107: Example 10
H1
R(s)
C(s)
Apply rule 2
Blocks in Parallel
G1
+
-
+
+
G2
G3
-
+
H3
-

## Slide 108: Example 10
H1
R(s)
C(s)
Apply rule 3
Elimination of Feedback Loop
G1
+
-
+
+
G2
1+G3
H3
-
cont….

## Slide 109: Example 10
H1
R(s)
C(s)
Apply rule 8
Shift take off point after block
G1
+
-
+
+
1+G3
H3
-
G2
1  G2
cont….

## Slide 110: Example 10
H1
R(s)
C(s)
Apply rule 1
Blocks in series
G1
+
-
+
+
1+G3
H3
-
G2
1  G2
1
1  G3
cont….

## Slide 111: Example 10
H1
R(s)
C(s)
Apply rule 2
Blocks in Parallel
G1
+
-
+
+
H3
-
G2(1  G 3) 1  G2
1
1  G3
cont….

## Slide 112: Example 10
H1
R(s)
C(s)
Apply rule 1
Blocks in Series
G1
+
-
-
G2(1  G 3) 1  G2
H 2 
1
1  G3
cont….

## Slide 113: Example 10
R(s)
C(s)
Apply rule 3
Elimination of Feedback loop
G1
+
-
-
G2(1  G 3) 1  G2
H1(H 2  H 2 G 3  1) 1  G3
cont….

## Slide 114: Example 10
R(s)
C(s)
Apply rule 1
Blocks in series
G1
G2(1  G 3)
1  G2  G2H1(1  H 2  H 2 G 3)
cont….

## Slide 115: Example 10
R(s)
C(s)
G1G2(1  G 3)
1  G2  G2H1(1  H 2  H 2 G 3)
cont….

## Slide 116: Example 10
R(s)
G1G2(1  G 3)
C(s) 
1  G2  G2H1(1  H 2  H 2 G 3)
cont….

## Slide 117: References
Control System Engineering
  J. J. Nagrath, M. Gopal
Feedback Control System
  R. A. Barapate
Control
Modern Engineering
- K. Ogata
117

## Slide 118: Thank You
118